## Slide 1
To Update or Not To Update? Bandwidth-Efficient
Intelligent Replacement Policies for DRAM Caches
Vinson Young
Moinuddin Qureshi
Notes: I am Vinson Young. This work is done with my collaborator Prashant Nair, and advisor Moinuddin Qureshi.
My working is on DICE: Compressing DRAM caches for bandwidth and capacity.

## Slide 2: MOORE’s LAW HITS Memory WALL
Need solutions for increased memory bandwidth and capacity
Channel
Bandwidth demand
On-Chip
Capacity demand
Notes: Bandwidth demand has been steadily increasing. Therefore, we need practical solutions for increasing memory bandwidth

## Slide 3: Emerging Memory technologies
Memory Bandwidth
high
low
Memory Capacity
small
large
3D-DRAM
DRAM
3D-XPoint(NVM)
Emerging memory technologies offer bandwidth/capacity tradeoffs
Notes: 3D-DRAM 4-8x bandwidth
3D-XPoint 4-8x capacity

## Slide 4: DRAM as a CACHE
OS-visible Space
System Memory
(DRAM / NVM)
DRAM-Cache
(3D-DRAM / DRAM)
Memory Hierarchy
fast
slow
CPU
L1$
L2$
L3$
CPU
L2$
L1$
Using DRAM as a DRAM-cache, can improve memory bandwidth and capacity (and avoid OS/software change)
MCDRAM from Intel
Optane DC from Intel
HBCC from AMD
Notes: One way to use the high-bandwidth memory is to architect as a cache, between system memory and L3, to invisibly speed up applications.
Note that this type of organization is already used in today’s Intel Knights Landing MCDRAM (Multi-Channel DRAM), and AMD’s High-Bandwidth Cache.
Improving DRAM caches would have practical impacts on today’s large-scale systems.

## Slide 5: ARCHITECTING LARGE DRAM CACHES
Organize at line granularity (64B) for high cache utilization
Gigascale cache needs large tag-store (tens of MBs)
3D-DRAM
2GB Data
64 MB
Tags
Tags?
Too large for SRAM
Notes: (E.g. 2GB DRAM cache needs ~64MB tag store (2 bytes/line))

## Slide 6: ARCHITECTING LARGE DRAM CACHES
Organize at line granularity (64B) for high cache utilization
Gigascale cache needs large tag-store (tens of MBs)
Practical designs must store Tags in DRAM
3D-DRAM
How to architect tag-store for low-latency tag access?
2GB Data
64 MB
Tags
Notes: (E.g. 2GB DRAM cache needs ~64MB tag store (2 bytes/line))

## Slide 7: Background: DRAM Cache Organization
Base DRAM Cache is 64B line-size, store Tag-With-Data, and are direct-mapped, to optimize for hit-latency. Can have low hit-rate. Can replacement policies help?
T
Data
Tag-With-Data (e.g., Alloy Cache)
Single Tag+Data Lookup (1x hit latency),
but direct-mapped and needs lookup on miss
This Tag-With-Data approach is used in Intel Knights Landing Product (MCDRAM)
T
Data
T
Data
T
Data

## Slide 8: Background: DRAM Cache repl is stateless
Install
Bypass
Always-Install
100%
LRU
DIP/BAB
Set-Duel
Bimodal Install
10%
BIP
90%
Recency-Based Replacement:
LRU is Always-Install
Probabilistic Replacement:
BIP is 90%-bypass, protect working set
Dueling Based Replacement:
DIP/BAB chooses best policy
Stateless global bypass policies can improve hit-rate and save install bandwidth.

## Slide 9: Performance of Stateless policy
Chart: 
Bandwidth-Aware Bypass | 0.026
State-in-SRAM RRIP | 0.21
Speedup*
DRAM Cache bypass can improve performance. But, global policies are too coarse grain to provide significant benefits
Bandwidth-Aware Bypass
3%
*System assumes 2GB HBM-based Cache, and PCM-based main memory (~4x latency).
Notes: We can DO BETTER.
Want a repl policy that can make decisions on a PER-LINE BASIS.
Let’s go through one.

## Slide 10: Desired Behavior from Cache Replacement
hit
hit
hit
hit
hit
miss
miss
miss
miss
miss
  Thrash-Resistance: Working set larger than cache  Preserve some of working set
  Scan-Resistance: Recurring scans  Preserve frequently-referenced working set
hit
hit
hit
hit
scan
scan
scan
hit
hit
hit
Wsize
LLCsize
[ RRIP (ISCA’10)]
Notes: Under both these scenarios, the desired behavior from cache replacement is as follows:
If working set is larger than cache, preserve some of it in the cache.
In the presence of recurring scans, the replacement policy should preserve the frequently referenced working set in the cache.

## Slide 11: Most effective policies are stateful (RRIP)
00
01
10
11
Hit
All Counters < 3
1. Install
2. Hit
Evict
Hit
[ Jaleel et al., ISCA’10 ]
Per-line RRIP protects against thrash and scans.
But, RRIP needs 2-bits per line and expensive state-update.
Lowest Priority
Highest
Priority
3. Age
Notes: First, describe how RRIP works. Need promote on hit. Need demote on bypass.
Then, describe the bandwidth costs (Promote. Demote). In SRAM, bandwidth cost is fine. But in DRAM….
/// 2GB needs 8MB
Since our work builds on top of the re-reference interval framework, I would like to quickly review the RRIP replacement policy. Like LRU which holds the LRU position with each cache line, RRIP replaces the notion of the “LRU” position with a prediction of the likely re-reference interval of a cache line. For example, with 2-bit RRIP, there are four possible re-reference intervals. If a line has re-reference interval 0, it implies the line will be re-referenced soon. If a line has re-reference interval 3, it implies the line will be re-referenced in the distant future. In between distant and immediate there is intermediate and far re-reference intervals.
When selecting a victim, RRIP always selects lines that have a distant re-reference interval for eviction. If no line is found, the states of all lines in the set are incremented until a line with distant re-reference interval is found.
When inserting new lines in the cache, scan-resistant SRRIP dynamically tries to learn the re-reference interval of a line by initially inserting ALL lines with “far” re-reference interval. This is done in an effort to dynamically learn the blocks re-reference interval. If the line has no locality, it will be quickly discarded. However, if the line has locality, on the next re-reference the line is moved to have immediate state, hence preserving it in the cache for a longer time.

## Slide 12: Potential of idealized Stateful policy
Chart: 
Bandwidth-Aware Bypass | 0.03
State-in-SRAM RRIP | 0.2
Speedup
17% Potential
Bandwidth-Aware Bypass
Reuse-based Bypass (idealized)
3%
Per-line reuse-based bypassing has higher potential; however, it requires substantial bandwidth costs to upkeep
*System assumes 2GB HBM-based Cache, and PCM-based main memory (~4x latency).
Notes: SID 10%
SID 21%
We could be happy with 10%. Already better than prior art (3%).
But I’m greedy. I want that 21%, and I don’t want to pay for it.

## Slide 13: Enabling intelligent replacement Policy
  Goal: Formulate reuse-bypassing for direct-mapped caches, and reduce bandwidth costs needed to maintain per-line state

## Slide 14: Policy: RRIP Age-On-Bypass (RRIP-AOB)
00
01
10
11
Hit
Bypass
Install
Hit
Evict
Hit
[ Jaleel et al., ISCA’10 ]
Demote on Bypass
Promote on Hit
RRIP-AOB protects reused lines for 3 conflicts. Enables protecting reused lines, and eventually replacing cold lines
Bypass
Bypass
Note: state-update costs bandwidth
But, suffers high bandwidth cost to constantly update state
Notes: First, describe how RRIP works. Need promote on hit. Need demote on bypass.
Then, describe the bandwidth costs (Promote. Demote). In SRAM, bandwidth cost is fine. But in DRAM….
/// 2GB needs 8MB
Since our work builds on top of the re-reference interval framework, I would like to quickly review the RRIP replacement policy. Like LRU which holds the LRU position with each cache line, RRIP replaces the notion of the “LRU” position with a prediction of the likely re-reference interval of a cache line. For example, with 2-bit RRIP, there are four possible re-reference intervals. If a line has re-reference interval 0, it implies the line will be re-referenced soon. If a line has re-reference interval 3, it implies the line will be re-referenced in the distant future. In between distant and immediate there is intermediate and far re-reference intervals.
When selecting a victim, RRIP always selects lines that have a distant re-reference interval for eviction. If no line is found, the states of all lines in the set are incremented until a line with distant re-reference interval is found.
When inserting new lines in the cache, scan-resistant SRRIP dynamically tries to learn the re-reference interval of a line by initially inserting ALL lines with “far” re-reference interval. This is done in an effort to dynamically learn the blocks re-reference interval. If the line has no locality, it will be quickly discarded. However, if the line has locality, on the next re-reference the line is moved to have immediate state, hence preserving it in the cache for a longer time.

## Slide 15: Reduce Bandwidth Costs: Repl BW breakdown
Replacement Bandwidth:
Always-Install, bandwidth consumed in: Install
RRIP, bandwidth consumed for: Install, Promote state, Demote state
111%
24%
RRIP reduces install bandwidth, but costs additional bandwidth to maintain state (~13% speedup). Can we reduce bandwidth cost?
Notes: Replacement bandwidth, if you are interested.
24% Install necessary.
State-update increases this 5x what it should be.
We need to cut this.
Can we get away with updating FEWER lines?
Use it to guide the rest?
Will this work?

## Slide 16
Coresidency: A given page has many lines coresident.
Update state for only a Representative, and infer others state.
Reduce Bandwidth Costs—INSIGHT: Spatial Locality of reuse
Eviction Locality: Those coresident often have similar state on eviction
78% also likely to be evicted
Notes: // add graphs. Individual ones.
Coresidency denotes spatial locality. But not perfect.

## Slide 17: Reduce Bandwidth Costs: Example
Access: Page A, Page B, Page B
A, RRPV=2
Set 0
B, RRPV=2
A, RRPV=3
A, RRPV=2
Set 1
B, RRPV=2
A, RRPV=2
A, RRPV=2
Set 2
B, RRPV=2
A, RRPV=2
A, RRPV=2
Set 3
B, RRPV=2
A, RRPV=2
Install A (4)
Bypass B (1)
Install B (4)
Time = 0
Time = 1
Time = 2
First conflicting set
Avoid 3 updates
Update 1
BW cost:
Efficient Tracking of Reuse (ETR) on RRIP-AOB, opportunistically reduces state-update based on spatial locality:
provides similar install policy, at reduced bandwidth cost
Follow

## Slide 18: Reduce Bandwidth Costs: ETR Implementation
Page Address
Last Bypass
Decision
Recent Bypass Table (RBT)
Page #
A
1. Hit, is follower,
follow representative’s decision
Page A
1
C
1. Miss, is representative,
make new decision
2. Update RRIP state
3. Update RBT
Page C
0
Page B
0
128-entry table (512B) is sufficient to implement ETR

## Slide 19: Reduce Bandwidth Costs: ETR REPLacement BW
RRIP-AOB [left] and ETR on RRIP-AOB [right], normalized to Always-Install
-70%
Update BW
ETR-RRIP reduces 70% of the state-update cost

## Slide 20: RRIP-AOB and Efficient Tracking of Reuse (speedup)
Chart: 
Bandwidth-Aware Bypass | 0.026
State-in-DRAM RRIP | 0.13
State-in-SRAM RRIP | 0.18
State-in-SRAM RRIP2 | 0.2
Speedup
Bridge 90% Gap
Bandwidth-Aware Bypass
RRIP-AOB
ETR on RRIP-AOB
ETR on RRIP-AOB enables intelligent replacement at low BW and storage costs (<1KB SRAM for RBT) to enable 18% speedup
Reuse-based Bypass (idealized)
*System assumes 2GB HBM-based Cache, and PCM-based main memory (~4x latency).

## Slide 21: intelligent Replacement for DRAM cache
BW-efficient reuse-based bypassing enables 18% speedup with <1KB SRAM (within 2% speedup of ideal w/ 8MB SRAM)
Intelligent Replacement:
with RRIP Age-On-Bypass
Reduced State-Update Cost: with Spatial Following

## Slide 23: Methodology (1/8th Knights Landing)
Stacked DRAM
Non-volatile Memory
 | Stacked DRAM | NVM (PCM-based)
Capacity | 2GB | 64GB
Bus | DDR 1.0GHz, 128-bit | DDR 2.0GHz, 64-bit
Channels | 4 channels | 1 channel
Bandwidth | 64 GBps | 16 GBps
Latency | 13~30 ns | 13~143 ns
CPU
(8 cores)
Notes: 1GB stacked DRAM.
4 channels, with 128-bit bus-width. ~100 GBps (1/8th of KNL bandwidth)
Iso-latency with DRAM, given current HBM products.
32GB DIMM-based DRAM