## Slide 1
TicToc: Enabling Bandwidth-Efficient DRAM Caching for Hybrid Memory Systems
Vinson Young
Zeshan Chishti
Moinuddin Qureshi

## Slide 2: MOORE’s LAW HITS Memory WALL
Need solutions for increased memory bandwidth and capacity
Channel
Bandwidth demand
On-Chip
Capacity demand
Notes: Bandwidth demand has been steadily increasing. Therefore, we need practical solutions for increasing memory bandwidth

## Slide 3: Emerging Memory technologies
Memory Bandwidth
high
low
Memory Capacity
small
large
3D-DRAM
DRAM
3D-XPoint(NVM)
Emerging memory technologies offer bandwidth/capacity tradeoffs
Notes: 3D-DRAM 4-8x bandwidth
3D-XPoint 4-8x capacity

## Slide 4: DRAM as a CACHE
OS-visible Space
System Memory
(DRAM / NVM)
DRAM-Cache
(3D-DRAM / DRAM)
Memory Hierarchy
fast
slow
CPU
L1$
L2$
L3$
CPU
L2$
L1$
Using DRAM as a DRAM-cache, can improve memory bandwidth and capacity (and avoid OS/software change)
MCDRAM from Intel
Optane DC from Intel
HBCC from AMD
Notes: One way to use the high-bandwidth memory is to architect as a cache, between system memory and L3, to invisibly speed up applications.
Note that this type of organization is already used in today’s Intel Knights Landing MCDRAM (Multi-Channel DRAM), and AMD’s High-Bandwidth Cache.
Improving DRAM caches would have practical impacts on today’s large-scale systems.

## Slide 5: Setup: Shared-channel DRAM cache for 3d-XPoint
3D-DRAM
DRAM Cache
Controller
Memory
Controller
DRAM
CPU Chip
3D-DRAM Cache for DRAM
Bandwidth for DRAM Cache Maintenance (e.g., miss probe)
DDR4
HBM
Cache +
Memory
Controller
DRAM
3D-XPoint
(b) DRAM Cache for 3D-XPoint
CPU Chip
DDR4
DRAM cache maintenance now steals memory bandwidth.
All cache bandwidth costs important
Channel sharing = Better pin utilization!
BW lost due to cache maintenance not necessarily impactful
Cache maintenance now consumes channel BW, can hurt
Notes: Proportion bar (x% of BW is for servicing Hits, Miss probe, etc)

## Slide 6: Challenge: DRAM Cache Maintenance Bandwidth
DRAM R
Hit path
Data
3D-XPoint R
Miss path
DRAM R
Miss probe
DRAM W
Data
Cache Install
Useful = cache hit, cache writeback, mem read, mem write
Poor data reuse can waste 66% channel bandwidth
Tag-Inside-Cacheline (TIC)
Current TIC/Alloy/KNL DRAM cache design can waste channel bandwidth, need to improve BW

## Slide 7: Background: Options for DRAM Cache TagS
TIC has good hits, TOC has good misses.
Use TIC for hit, TOC for miss, for best of both?
T
Data
Approach 1: Tag-Inside-Cacheline (Alloy Cache)
Hit: 1 access
Miss: 1 access
T
Data
T
Data
T
Data
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
SRAM Tag Cache
(32KB)
Data
Data
Data
Data
Approach 2: Tag-Outside-Cacheline (Timber Cache)
 Hit: 1+ρ accesses
 Miss: ρ accesses
Fetch on TC miss
ρ = Probability of Tag-Cache Miss
* Writeback, Install, Dirty-evict probe to be discussed later
Hit: 2 accesses
Miss: 1 access

## Slide 8: Initial Proposal: Dual tags with TICTOC
T
Data
T
Data
T
Data
T
Data
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
Tag
Cache
Hit/Miss Pred
Pred Miss, Use TOC
Common case is using TIC for hits, TOC for misses. Saves both hit and miss bandwidth
Pred Hit, Use TIC
Pred-hit, actual-hit: 1 access
Pred-hit, actual-miss: 1 access (rare)
Pred-miss, actual-hit: 1+ρ accesses (rare)
Pred-miss, actual-miss: ρ accesses

## Slide 9: Initial Proposal: TICTOC Performance
Chart: Speedup w.r.t TIC
| mcf | lbm | soplex | libq | gems | omnet | wrf | gcc | xalanc | zeus | cactus | cc twi | pr twi | Gmean | + no mcf
TOC | 0.308 | 1 | 0.796 | 0.996 | 0.829 | 0.304 | 0.968 | 0.715 | 0.298 | 0.634 | 0.867 | 1.401 | 1.441 | 0.72044 | 0.865
TicToc | 0.346 | 1.041 | 0.83 | 1.008 | 0.855 | 0.329 | 0.998 | 0.815 | 0.322 | 0.858 | 1.176 | 1.408 | 1.447 | 0.78863 | 0.942
SRAM Tags | 1.288 | 1.072 | 1.109 | 1.024 | 1.162 | 1.008 | 1.085 | 1.065 | 1.028 | 1.148 | 1.235 | 1.449 | 1.48 | 1.1567 | 1.135
Combining TIC and TOC is worse than TIC individually, why?
TIC
*System assumes 4GB DRAM Cache and 3D-XPoint-based main memory, sharing channels.

## Slide 10: Problem: Channel Bandwidth Consumption
DRAM R
3D-XPoint R
Hit path
Miss path
DRAM R
Miss probe
DRAM W
Data
Data
Cache Install
Tag-Inside-Cacheline (TIC)
(KBs SRAM)
DRAM W
Data
Writeback path
Tag-Outside-Cacheline (TOC)
(KBs SRAM)
DRAM R
3D-XPoint R
Hit path
Miss path
DRAM W
Data
Data
Install
DRAM W
Data
Writeback path
R
TagFetch
R
TagFetch
R
TagFetch
Poor Miss
Good Hit
Poor Hit
Good Miss
Poor WB
TicToc
(KBs SRAM)
DRAM R
3D-XPoint R
Hit path
Miss path
DRAM W
Data
Data
Install
DRAM W
Data
Writeback path
R
TagFetch
R
TagFetch
Good Miss
Poor WB
Good Hit
Good WB

## Slide 11: Problem: high TOC dirty-bit updates
TicToc has reduced miss BW, but higher TOC dirty-bit update BW
Tag-Inside-Cacheline BW Consumption
TicToc BW Consumption

## Slide 12: Main Contribution: Inexpensive dirty-bit Tracking
Dirty-bit maintenance has poor spatial locality and costs substantial bandwidth to maintain.
Goal: Enable effective dirty-bit tracking to make a bandwidth-efficient DRAM cache.

## Slide 13: Proposal 1: Reducing repeated TOC Dirty-bit CHECKS with DRAM Cache Dirtiness bit
Desired: Know L4 dirty-status to avoid TOC dirty-bit check
100 Data,1 TOC-dirty-check,1 TOC-dirty-update = 102!
L4 DRAM-Cache
Clean A
L4 DRAM-Cache
Dirty A
TOC check necessary only for
Clean->Dirty transition
Mechanism: Remember L4 dirty information alongside L3 line!
–Store DRAM-Cache Dirtiness (DCD) bit alongside L3 lines.
–Set on read of dirty line from DRAM Cache.
–Check&Update TOC dirty-bit only when L4-line clean  L4 dirty
DCD bit ensures that repeated writebacks do not need to check TOC dirty-bit
Example (100 writes):100 Data,100 TOC-dirty-check,1 dirty-update

## Slide 14: Proposal 2A: Reducing Initial TOC Dirty-bit update with Preemptive dirty marking
Preemptive dirty marking 1. improves dirty-bit update cost for written lines, but 2. degrades miss cost for unwritten lines.
Ideally, should use PDM only for likely-to-be-written lines
(a) Write Path
Install
Writeback
TOC Metadata Maintenance
|D
|C
TIC
Meta R
Meta W
TOC
D| .
C| .
(b) Miss + Install Path
Miss/WB Probe
Mem Read
Install
|C
Mem R
Cache W
TIC
Mem R
Cache W
TOC
D|D
= (TOC Dirty-bit | TIC Dirty-bit). C is clean, D is dirty
= access
TicToc
D|D
C|C
Meta R
Meta W
Mem R
Cache W
TicToc
Marking lines dirty at install coalesces tag&dirty update  reduce BW for dirty
Marking clean lines as TOC-dirty increases miss BW
D|C
Mem R
Cache W
TicToc (+PDM)
TicToc (+PDM)
D|D
D|C
“Predicted-Dirty”
Read in preparation for dirty eviction
Need dynamic solution!

## Slide 15: Proposal 2B: pC-based Dirty prediction
Inspired by Signature-based Hit Predictor (SHiP/SHiP++). Use Install-PC as Sig
PC-based write predictor learns which PC’s install likely-to-write lines. Good prediction enables saving both miss bandwidth and dirty-bit update.
DRAM Cache
Install-PC + Written-To
(a) Observe write behavior for PCs
SRAM Counter Table
(~1KB storage)
PC-indexed Counter Table
(b) Learn PCs corresponding to write
At Install, predict likely-to-write:
1. Index Ctr-table with PC
2. Predict write behavior with PC
3. If predict write,
mark TOC dirty-bit and DCD
(c) Predict write behavior based on PC
C. Wu, A. Jaleel, W. Hasenplaugh, M. Martonosi, S. Steely, J. Emer, “SHiP,” in MICRO’11.
V. Young, A. Jaleel, C. Chou, M. Qureshi, “SHiP++,” in CRC-2 in ISCA’17.

## Slide 16: Results: DIRTY Misclassification Rate
Low misclassification rate (~10% ratio) ensures low miss-probe
and low dirty-bit update BW cost
Chart: Prediction Breakdown (%)
| mcf | lbm | soplex | libq | gems | omnet | wrf | gcc | xalanc | zeus | cactus | cc twi | pr twi | Gmean
PDirty,ADirty | 0.9 | 53.2 | 9.8 | 8 | 59.3 | 34.1 | 62.4 | 80.7 | 96.5 | 66.1 | 73.4 | 4 | 9.7 | 42.931
PClean,ADirty | 0.8 | 4.7 | 5.6 | 15.8 | 6.3 | 2 | 21.4 | 3.6 | 0.6 | 12.9 | 0.4 | 0 | 0 | 5.7
PClean,AClean | 98.1 | 37 | 84.3 | 61.6 | 33.7 | 59.5 | 13.4 | 13.6 | 1 | 20.2 | 25.4 | 95.8 | 90.2 | 48.754
PDirty,AClean | 0.2 | 5 | 0.2 | 14.6 | 0.6 | 4.4 | 2.8 | 2.1 | 1.9 | 0.8 | 0.8 | 0.1 | 0.1 | 2.585
Chart: Misclassification Ratio (%)
| mcf | lbm | soplex | libq | gems | omnet | wrf | gcc | xalanc | zeus | cactus | cc twi | pr twi | Gmean
PClean,ADirty | 0.8 | 4.7 | 5.6 | 15.8 | 6.3 | 2 | 21.4 | 3.6 | 0.6 | 12.9 | 0.4 | 0 | 0 | 5.7
PDirty,AClean | 0.2 | 5 | 0.2 | 14.6 | 0.6 | 4.4 | 2.8 | 2.1 | 1.9 | 0.8 | 0.8 | 0.1 | 0.1 | 2.585

## Slide 17: RESULTS: TICTOC speedup
Chart: Speedup w.r.t. TIC
| mcf | lbm | soplex | libq | gems | omnet | wrf | gcc | xalanc | zeus | cactus | cc twi | pr twi | Gmean | + no mcf
TOC | 0.308 | 1 | 0.796 | 0.996 | 0.829 | 0.304 | 0.968 | 0.715 | 0.298 | 0.634 | 0.867 | 1.401 | 1.441 | 0.72044 | 0.865
TicToc | 0.346 | 1.041 | 0.83 | 1.008 | 0.855 | 0.329 | 0.998 | 0.815 | 0.322 | 0.858 | 1.176 | 1.408 | 1.447 | 0.78863 | 0.942
TicToc + DCD | 0.442 | 1.062 | 1.095 | 1.024 | 0.923 | 0.968 | 1.054 | 0.979 | 0.87 | 0.888 | 1.205 | 1.412 | 1.446 | 0.9938 | 1.086
TicToc + PDM | 0.442 | 1.062 | 1.095 | 1.018 | 1.059 | 0.975 | 1.066 | 1 | 0.974 | 1.084 | 1.218 | 1.416 | 1.452 | 1.0329 | 1.112
SRAM Tags | 1.288 | 1.072 | 1.109 | 1.024 | 1.162 | 1.008 | 1.085 | 1.065 | 1.028 | 1.148 | 1.235 | 1.449 | 1.48 | 1.1567 | 1.135
TicToc (34KB SRAM) eliminates most bandwidth spent for Tag-Maintenance, to enable speedup near SRAM Tag approach (~20MB)
*System assumes 4GB DRAM Cache and 3D-XPoint-based main memory, sharing channels.
DRAM-Cache Dirtiness reduces dirty-bit update cost for repeated writes
Preemptive Dirty Marking reduces dirty-bit update cost for write-once lines

## Slide 18: Results: TICTOC Bandwidth Breakdown
TIC Baseline:
(suffers from miss probe)
TicToc with DCD+PDM:
(reduces miss probe and tag maintenance)
TicToc tag organization eliminates most tag-maintenance BW.
Now, install bandwidth significant.

## Slide 19: Reducing Install BW with Write-aware bypass
Read Miss
90%-Bypass
(save install/tag BW)
Write Miss
Always-Install
(reduce 3D-XPoint writes)
Pred-Clean
Pred-Dirty
Write-Predictor
= Preemptive Write-Allocate
And, proactively installing likely-dirty lines coalesces more metadata updates
Preferentially bypass clean lines to save install bandwidth

## Slide 20: Putting it all together: Cache BW Reduction
TIC Baseline:
(suffers from miss probe,
suffers from install BW)
+ TicToc:
(reduces miss probe,
suffers from install BW)
+ Write-Aware Bypassing:
(reduces install BW)
Combination of approaches increases fraction of useful BW to 90%!

## Slide 21: Write-aware bypass performance
Chart: Speedup w.r.t TIC
| mcf | lbm | soplex | libq | gems | omnet | wrf | gcc | xalanc | zeus | cactus | cc twi | pr twi | Gmean
No DRAM Cache | 1.212 | 0.814 | 1.077 | 0.852 | 1.173 | 0.646 | 0.962 | 0.961 | 0.536 | 1.036 | 1.125 | 1.706 | 2.138 | 1.0287
TicToc | 0.442 | 1.062 | 1.095 | 1.018 | 1.059 | 0.975 | 1.066 | 1 | 0.974 | 1.084 | 1.218 | 1.416 | 1.452 | 1.0329
+ 90%-Bypass | 1.135 | 1.124 | 1.238 | 1.008 | 1.316 | 0.966 | 1.082 | 0.976 | 0.836 | 1.109 | 1.243 | 1.685 | 2.019 | 1.1776
+ Write-Allocate | 1.115 | 1.144 | 1.293 | 1.061 | 1.291 | 0.994 | 1.19 | 1.028 | 0.873 | 1.001 | 1.509 | 1.784 | 2.087 | 1.2216
+ Preemptive Write-Allocate | 1.118 | 1.072 | 1.298 | 1.04 | 1.333 | 0.995 | 1.123 | 1.059 | 0.967 | 1.262 | 1.505 | 1.808 | 2.206 | 1.2526
Write-Aware Bypass reduces install bandwidth without sacrificing
write buffering capabilities, for 25% speedup
90%-bypass reduces install bandwidth, but increases writes to 3D-XPoint (bad)
Preemptive Write-Allocate reduces installs, and retains write buffering ability
*System assumes 4GB DRAM Cache and 3D-XPoint-based main memory, sharing channels.

## Slide 22: Hardware Cost
TicToc Component | SRAM Storage | Paper
Hit-Miss Predictor | 1 KB | Alloy Cache
DRAM Cache Presence | 1 bit / L3-line | BEAR
Metadata Cache | 32 KB | TIMBER / Sim
DRAM Cache Dirtiness | 1 bit / L3-line | This work
Signature-based Write Predictor | 1 KB | This work
TicToc Total | 34KB + 2 bits / L3-line | 
TicToc achieves its benefits with minimal hardware requirements
TicToc Component | SRAM Storage | Paper
Hit-Miss Predictor | 1 KB | Alloy Cache
DRAM Cache Presence | 1 bit / L3-line | BEAR
Metadata Cache | 32 KB | TIMBER / Sim

## Slide 23: Thank you
TicToc solves hit and miss bandwidth.
DRAM Cache Dirtiness + Preemptive Dirty Marking solves dirty-bit tracking bandwidth.
Write-aware bypass solves install bandwidth.
TicToc enables a cheap (low SRAM cost ~32KB), high-performance (>90% utilization of bus bandwidth) DRAM cache for heterogeneous memories.

## Slide 25: Methodology (1/8th Knights Landing)
DRAM
3D-XPoint NVM
 | DRAM | 3D-XPoint
Capacity | 2GB | 64GB
Bus | DDR 2.0GHz, 64-bit | DDR 2.0GHz, 64-bit
Channels | 1 channel, shared | 1 channel, shared
Bandwidth | 16 GBps, shared | 16 GBps, shared
Latency | 13~30 ns | 13~96R~320W ns
CPU
(8 cores)
Notes: 1GB stacked DRAM.
4 channels, with 128-bit bus-width. ~100 GBps (1/8th of KNL bandwidth)
Iso-latency with DRAM, given current HBM products.
32GB DIMM-based DRAM