## Slide 1: New Attacks and Defense for Encrypted-Address Cache
Moinuddin Qureshi
ISCA-2019

## Slide 2: The Spy Problem
How many retreats to identify all the spies?
There are A agents at intelligence agency and S of them are spies. Find the spies.
You can send a given number of agents to a “retreat” on an island.
If all S spies are present at the retreat, they meet to strategize.
If even one spy is missing, this spy meeting will not take place.
The only information you get is if the spy meeting happened.
You can send any number of agents to the retreat. A=1024 and S=17.

## Slide 3: The Spy Problem: Basic Solution
Single Holdout Method (SHM) needs ~A retreats, total cost O(Agents^2)
Holdout one agent, send rest to retreat. If meeting, holdout not spy, else spy
(R=1)
(R=2)
(R=3)
(R=A)
…

## Slide 4: The Spy Problem: Efficient Solution
Group Elimination Method has cost in the O(A*S) – 40x lower than SHM
Divide in G groups. Hold out group. If meeting, discard the entire group.
(R=1)
(R=2)
(R=3)

## Slide 5: Outline
Spy Problem
CEASER
New Attacks
Defense

## Slide 6: Conflict-Based Cache Attacks
B
LLC
CORE
(Spy)
CORE
(Victim)
A
B
V
Co-running spy can infer access pattern of victim by causing cache conflicts
Conflicts leak access pattern, used to infer secret [AES – Bernstein’05]
Miss for B
Victim Accessed Set

## Slide 7: Prior Solutions
Way Partitioning
Mapping Table
(MT)
NoMo [TACO’12], CATalyst [HPCA’16]
Table-Based Randomization
RPCache[ISCA’07], NewCache[MICRO’08]
Not scalable to many core
Mapping Table large for LLC (MBs)
OS support needed to protect Table
Inefficient use of cache space

## Slide 8: CEASER: Randomization without Tables
Robust to attacks (years)
Negligible slowdown (~ 1%)
No OS support needed
Negligible storage (24 bytes)
Localized change (within cache)
Cache
Line Address
Encrypt
Key1
Key2
Change Key, Periodically
CEASER uses Encrypted Address + Remapping [MICRO 2018]
Remap Rate of 1% sufficient to provide robustness of years

## Slide 9: Anatomy of the Attack
Attacker needs an efficient search algorithm to form eviction set
LLC
X
Find “L” random lines that can cause conflict miss on target set
Step-1: Trial-and-Error
Use a search algorithm, find “W+1” conflicting lines in L
Step-2: Search Algorithm
Launch conflict-based attack until the lines get remapped
Step-3: Launch Attack
Notes: TODO: Make this animated

## Slide 10: State-of-the-Art Search Algorithm (SHM)
D
A
C
B
LLC
X
Single Holdout Method (SHM): for L=1200, W=16, need about 1M accesses Can we develop faster attacks than state-of-the-art?
[Liu et al. S&P, 2015]
Form pattern such that cache has a conflict miss
Removed line NOT
in conflicting set
Removed line MAPS
to conflicting set
Remove one line from pattern & check conflict
Conflict Miss?
No
Yes
Notes: TODO: Make this animated

## Slide 11: Outline
Spy Problem
CEASER
New Attacks
Defense

## Slide 12: Attack-1: Fast Search Algorithm (GEM)
Group Elimination Method : L=1200, W=16, accesses reduced from 1M to 40K
 Remap Rate of CEASER must be increased to >25% to mitigate GEM
Divide L in “W+1” groups. Hold out group. If conflict, discard the group.
(R=1)
(R=2)
(R=3)
Notes: TODO: Make this animated

## Slide 13: Attack-2: Exploit Replacement Policy
Attack-2 avoids search algorithm : L=1200, accesses reduced from 1M to ~3K
 Remap Rate of CEASER must be increased to >100%
LRU susceptible to thrashing. Exploit property to avoid search algorithm
D
A
C
B
LLC
X
A
B
C
D
X
A
B
C
D
X
Access Pattern to Attack LRU
3 misses, all to conflicting set
No need for search algorithm
A
B
C
D
X
A
B
C
D
X
A
B
C
D
X
Access Pattern to Attack RRIP
Notes: TODO: Make this animated

## Slide 14: Outline
Spy Problem
CEASER
New Attacks
Defense
Goal: Tolerate Fast Attacks with CEASER while having low Remap-Rate

## Slide 15: Skewed-Cache: Diversity of Locations
Skewed-Cache enables line to map to different sets. Static hash insecure.
A
B
Set-Associative Cache
X
X?
X?
Skewed Cache
A/B
h2
h1
A/B
X
The Good:
Map to different sets
Need (for security):
Unpredictable hashes
Dynamic changing hashes

## Slide 16: Skewed-CEASER
Attacker needs to dislodge target line from multiple possible locations
Skewed-CEASER with 2+ partitions possible (stronger security)
Enable CEASER to map lines to different sets via principles of skewing
Notes: We combine. We do not use different hash functions but only different sets of keys. At miss the line is randomly installed in either of the two halves. The attacker now needs to dislodge the line from multiple possible locations.

## Slide 17: Security Analysis
Skewed-CEASER can tolerate years of attack (with Remap-Rate of 1%)
Time to get enough number of “hard conflict” lines (dislodge both locations)
X?
X?
A/B
A/B
Remap-Rate | 8MB LLC | 1 MB LLC-Bank
1% (default) | 1 ms per 100+ years | 1 ms per 18 years
0.5% | 1 ms per 100+ years | 1 ms per day
0.1% | 1 ms per 68 years | 1 ms per second
Notes: EMPHASIZE 1% (POWER, ENERGY, PERFORAMNCE, MISSRATE)

## Slide 18: Performance and Storage Overheads
Skewed-CEASER incurs negligible slowdown (~1% ) & overheads (<100 bytes)
Chart: 
CEASER | 99.27 | 98.98 | 99.127
Skewed-CEASER | 99.42 | 99.21 | 99.31
Rate-34
Mix-34
ALL-68
Norm Performance (%)
8 cores with 8MB LLC 16-way
(34 workloads, SPEC + Graph)
Structures | Cost
CEASER | 24 bytes
Skewed-CEASER (2) | 48 bytes
Skewed-CEASER (4) | 96 bytes

## Slide 19: Summary
Skewed-CEASER has flexibility in placement of line, increased robustness
(performance and storage overhead remains negligible)
Cache randomization makes it harder for the adversary to form eviction sets
Attack-1: Fast search algorithm (GEM)
Attack-2: Exploit replacement policy, avoid search
Defense: Skewed-CEASER = CEASER + Skewed-Cache
Concurrent Paper
IEEE S&P, May 2019
Skewed Cache (Static)
USENIX Security, Aug 2019