## Slide 1: Low-Cost Inter-Linked Subarrays (LISA) Enabling Fast Inter-Subarray Data Movement in DRAM
Kevin Chang Prashant Nair, Donghyuk Lee, Saugata Ghose, Moinuddin Qureshi, and Onur Mutlu

## Slide 2: Problem: Inefficient Bulk Data Movement
Bulk data movement is a key operation in many applications
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]
Memory Controller
CPU
Memory
Channel
dst
src
Long latency and high energy
LLC
Core
Core
Core
Core
64 bits

## Slide 3: Moving Data Inside DRAM?
DRAM cell
Subarray 1
Subarray 2
Subarray 3
Subarray N
…
Internal Data Bus (64b)
8Kb
512 rows
Bank
Bank
Bank
Bank
DRAM
…
Low connectivity in DRAM is the fundamental bottleneck for bulk data movement
Goal: Provide a new substrate to enable wide connectivity between subarrays

## Slide 4: Key Idea and Applications
Low-cost Inter-linked subarrays (LISA)
  Fast bulk data movement between subarrays
  Wide datapath via isolation transistors: 0.8% DRAM chip area
LISA is a versatile substrate → new applications
Subarray 1
Subarray 2
…
  Fast bulk data copy: Copy latency 1.363ms→0.148ms (9.2x) → 66% speedup, -55% DRAM energy
  In-DRAM caching: Hot data access latency 48.7ns→21.5ns (2.2x) → 5% speedup
  Fast precharge: Precharge latency 13.1ns→5.0ns (2.6x) → 8% speedup

## Slide 5: Outline
Motivation and Key Idea
DRAM Background
LISA Substrate
  New DRAM Command to Use LISA
Applications of LISA

## Slide 6: DRAM Internals
Bank (16~64 SAs)
Bitline
Row Buffer
Sense amplifier
S
S
S
S
S
Precharge unit
P
P
P
P
P
Row Decoder
Wordline
Subarray
512 x 8Kb
I/O
64b
Internal Data Bus
8~16 banks per chip
Subarray

## Slide 7: DRAM Operation
To Bank I/O
ACTIVATE: Store the row into the row buffer
READ: Select the target column and drive to I/O
PRECHARGE: Reset the bitlines for a new ACTIVATE
S
P
S
P
S
P
S
P
1
1
1
1
Vdd/2
Vdd
Bitline Voltage Level:
1
2
3

## Slide 8: Outline
Motivation and Key Idea
DRAM Background
LISA Substrate
  New DRAM Command to Use LISA
Applications of LISA

## Slide 9: Observations
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
…
Bitlines serve as a bus that is as wide as a row
1
Bitlines between subarrays are close but disconnected
2
Internal Data Bus (64b)

## Slide 10: Low-Cost Interlinked Subarrays (LISA)
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
…
Interconnect bitlines of adjacent subarrays in a bank using isolation transistors (links)
ON
LISA forms a wide datapath b/w subarrays
64b
8kb

## Slide 11: New DRAM Command to Use LISA
Row Buffer Movement (RBM): Move a row of data in an activated row buffer to a precharged one
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
Subarray 1
Subarray 2
RBM: SA1→SA2
Vdd
Vdd
…
Vdd
Vdd/2
Vdd-Δ
Vdd/2+Δ
on
Charge
Sharing
Activated
Precharged
Amplify the charge
Activated
RBM transfers an entire row b/w subarrays

## Slide 12: RBM Analysis
The range of RBM depends on the DRAM design
  Multiple RBMs to move data across > 3 subarrays
Validated with SPICE using worst-case cells
  NCSU FreePDK 45nm library
4KB data in 8ns (w/ 60% guardband) → 500 GB/s, 26x bandwidth of a DDR4-2400 channel
0.8% DRAM chip area overhead [O+ ISCA’14]
Subarray 1
Subarray 2
Subarray 3

## Slide 13: Outline
Motivation and Key Idea
DRAM Background
LISA Substrate
  New DRAM Command to Use LISA
Applications of LISA
  1. Rapid Inter-Subarray Copying (RISC)
  2. Variable Latency DRAM (VILLA)
  3. Linked Precharge (LIP)

## Slide 14: 1. Rapid Inter-Subarray Copying (RISC)
Goal: Efficiently copy a row across subarrays
Key idea: Use RBM to form a new command sequence
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
Subarray 1
Subarray 2
Activate dst row (write row buffer into dst row)
3
RBM SA1→SA2
2
Activate src row
1
src row
dst row
Reduces row-copy latency by 9.2x, DRAM energy by 48.1x

## Slide 15: Methodology
Cycle-level simulator: Ramulator [CAL’15] https://github.com/CMU-SAFARI/ramulator
CPU: 4 out-of-order cores, 4GHz
L1: 64KB/core, L2: 512KB/core, L3: shared 4MB
DRAM: DDR3-1600, 2 channels
Benchmarks:
  Memory-intensive: TPC, STREAM, SPEC2006, DynoGraph, random
  Copy-intensive: Bootup, forkbench, shell script
50 workloads: Memory- + copy-intensive
Performance metric: Weighted Speedup (WS)

## Slide 16: Comparison Points
Baseline: Copy data through CPU (existing systems)
RowClone [Seshadri+ MICRO’13]
  In-DRAM bulk copy scheme
  Fast intra-subarray copying via bitlines
  Slow inter-subarray copying via internal data bus

## Slide 17: System Evaluation: RISC
Chart: Over Baseline (%)
| WS Improvement | DRAM Energy Reduction
RowClone | -23.9607 | 5.1182
RISC | 66.2 | 55.47
66%
55%
-24%
5%
Degrades bank-level parallelism
Rapid Inter-Subarray Copying (RISC) using LISA improves system performance

## Slide 18: 2. Variable Latency DRAM (VILLA)
Goal: Reduce DRAM latency with low area overhead
Motivation: Trade-off between area and latency
High area overhead: >40%
Long Bitline (DDRx)
Short Bitline (RLDRAM)
  Shorter bitlines → faster activate and precharge time

## Slide 19: 2. Variable Latency DRAM (VILLA)
Key idea: Reduce access latency of hot data via a heterogeneous DRAM design [Lee+ HPCA’13, Son+ ISCA’13]
VILLA: Add fast subarrays as a cache in each bank
Slow Subarray
Slow Subarray
Fast Subarray
LISA: Cache rows rapidly from slow to fast subarrays
32 rows
512 rows
Reduces hot data access latency by 2.2x at only 1.6% area overhead
Challenge: VILLA cache requires frequent movement of data rows

## Slide 20: System Evaluation: VILLA
Chart: Workloads (50)
VILLA | 0.99914 | 1.0049 | 1.0103 | 1.014 | 1.0151 | 1.0189 | 1.019 | 1.0199 | 1.0204 | 1.0206 | 1.0206 | 1.0218 | 1.0222 | 1.0225 | 1.0228 | 1.0229 | 1.0242 | 1.0249 | 1.0253 | 1.0272 | 1.0281 | 1.0297 | 1.0299 | 1.0304 | 1.0362 | 1.0394 | 1.0461 | 1.0461 | 1.0518 | 1.052 | 1.054 | 1.061 | 1.0622 | 1.0642 | 1.0646 | 1.0714 | 1.075 | 1.0754 | 1.0782 | 1.0816 | 1.0823 | 1.0839 | 1.0893 | 1.1018 | 1.1027 | 1.1039 | 1.112 | 1.1334 | 1.1446 | 1.1605
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
VILLA Cache Hit Rate | 0.8 | 8.3 | 16.3 | 8.7 | 14.4 | 16.7 | 21.5 | 8 | 23 | 16.7 | 32.8 | 15.4 | 16.8 | 26.5 | 18.8 | 26.7 | 23.1 | 29.2 | 19.4 | 18.3 | 20.1 | 30.7 | 23 | 24.7 | 18.6 | 26.6 | 40.2 | 36.2 | 39.7 | 33.8 | 50.1 | 39.2 | 33.7 | 38 | 41.5 | 43.1 | 38.4 | 41.6 | 43.9 | 40.4 | 52.9 | 35.4 | 37.6 | 45.9 | 49.8 | 49.9 | 61.3 | 52.7 | 64.9 | 69.1
Avg: 5%
Max: 16%
Caching hot data in DRAM using LISA
improves system performance
50 quad-core workloads: memory-intensive benchmarks

## Slide 21: 3. Linked Precharge (LIP)
Problem: The precharge time is limited by the strength of one precharge unit
Linked Precharge (LIP): LISA precharges a subarray using multiple precharge units
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
Precharging
S
P
S
P
S
P
S
P
Activated row
on
on
on
Linked Precharging
Conventional DRAM
LISA DRAM
Reduces precharge latency by 2.6x
(43% guardband)

## Slide 22: System Evaluation: LIP
Chart: Workloads (50)
LIP | 1.0297 | 1.0328 | 1.0356 | 1.0448 | 1.0464 | 1.0521 | 1.0561 | 1.0576 | 1.0585 | 1.0619 | 1.0622 | 1.0625 | 1.0642 | 1.0656 | 1.0675 | 1.0706 | 1.0706 | 1.0724 | 1.0727 | 1.0731 | 1.074 | 1.0741 | 1.0752 | 1.0798 | 1.0804 | 1.0839 | 1.0862 | 1.0866 | 1.0878 | 1.0886 | 1.0893 | 1.0907 | 1.0908 | 1.0918 | 1.0921 | 1.0931 | 1.0939 | 1.0966 | 1.0974 | 1.0979 | 1.1009 | 1.1081 | 1.109 | 1.1096 | 1.1149 | 1.1151 | 1.1228 | 1.1247 | 1.1312 | 1.1318
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Avg: 8%
Max: 13%
Accelerating precharge using LISA
improves system performance
50 quad-core workloads: memory-intensive benchmarks

## Slide 23: Other Results in Paper
Combined applications
Single-core results
Sensitivity results
  LLC size
  Number of channels
  Copy distance
Qualitative comparison to other hetero. DRAM
Detailed quantitative comparison to RowClone

## Slide 24: Summary
Bulk data movement is inefficient in today’s systems
Low connectivity between subarrays is a bottleneck
Low-cost Inter-linked subarrays (LISA)
  Bridge bitlines of subarrays via isolation transistors
  Wide datapath with 0.8% DRAM chip area
LISA is a versatile substrate → new applications
  Fast bulk data copy: 66% speedup, -55% DRAM energy
  In-DRAM caching: 5% speedup
  Fast precharge: 8% speedup
  LISA can enable other applications
Source code will be available in April https://github.com/CMU-SAFARI

## Slide 25: Low-Cost Inter-Linked Subarrays (LISA) Enabling Fast Inter-Subarray Data Movement in DRAM
Kevin Chang Prashant Nair, Donghyuk Lee, Saugata Ghose, Moinuddin Qureshi, and Onur Mutlu