## Slide 1
Enabling Transparent Memory-Compression for Commodity Memory Systems
HPCA 2019
Vinson Young*
Sanjay Kariyappa*
Moinuddin Qureshi
*These authors contributed equally to this work

## Slide 2: MOORE’s LAW HITS BANDWIDTH WALL
Need practical solutions for scaling memory bandwidth
Channel
Bandwidth demand
On-Chip
Notes: Bandwidth demand has been steadily increasing. Therefore, we need practical solutions for increasing memory bandwidth

## Slide 3: Mem Compression for capacity and Bandwidth
Data A
Data B
Data B
Compression frees up space to store more data, improves capacity
✔
Operating System
But, memory capacity fluctuates – needs OS support to utilize capacity
✘
Capacity benefits require OS support (multi-vendor) – hinders adoption.
 Instead, we focus solely on improving memory bandwidth, with
Transparent Memory Compression: HW compression for BW without OS
Physical Capacity
OS Mem Capacity
2
3
OS Mem Capacity
Phys Capacity
Notes: Compressed memory is an attractive approach to solve this problem
Compression allows for packing more lines in a physical amount of space, which improves memory capacity.
While this seems useful we haven't seen widespread adoption of compressed memory systems. The problem is that with compressed memory the capacity changes and we need OS support to adapt to this variable capacity. This means the MICROSOFT and the INTELs of the world will need to both agree for making compressed memory viable. We want the bandwidth benefits of compression in an OS-transparent manner.
With Transparent Memory Compression

## Slide 4: Transparent Memory Compression
½ Channel
½ Channel
Channel
Data A
Line A (bottom)
Line A (top)
Line B (compress)
Line A (bottom)
Line A (top)
Line B (compress)
e.g., Memzip*
Can read compressed lines with half bandwidth
M
M
M
M
M
M
M
M
✔
OS transparent
✘
Commodity Memory
✘
Negligible Metadata Overhead
Memzip
✔
Bandwidth Benefits
Current TMC proposals require non-commodity memory and require significant metadata overhead
TMC: Enable bandwidth benefits without OS support
*Ali Shafiee, Meysam Taassori, Rajeev Balasubramonian, & Al Davis. “Memzip” in HPCA 2014
Notes: TMC. BW without OS changes. Compress in place. E.g. Memzip.
Changes DIMM organization,
reorganize such that it takes Multiple accesses to read data.
Save on accesses when lines are compressible
Gets BW without OS. But, requires:
DIMM Changes, to support half line accesses
Expensive metadata accesses, to understand compressed mapping
Suffer from performance degradation when running incompressible workloads
Our work has a simple goal. We want more bandwidth out of commodity memory systems

## Slide 5: Goal: Practical transparent mem compression
Bandwidth Benefits
OS Transparent
Commodity Memory
Negligible Metadata Overhead
Robust Performance
✔
✔
✔
✔
Our goal is to enable Practical TMC – to obtain bandwidth benefits without the costs of compression. Should be OS transparent, use commodity memory, have minimal metadata access, and be robust.
✔
🗴
🗴
🗴
Notes: Goal of our paper is to improve memory bandwidth, without the costs of compression. Should be OS transparent, applicable to commodity memory, have negligible metadata overhead, and have robust performance under any circumstance.

## Slide 6: Overview
Background
Proposal
  Address Mapping
  In-line Metadata
  Location Prediction
Results
Dynamic Policy
Useful for
Commodity Memory

## Slide 7: Problem of TMC on commodity memories
Compressed Commodity Memory
No Partial-line Transfers in Commodity Memory
Channel
Line B
Data A
Line B
Data A
TMC on commodity memory does not improve memory bandwidth
Line A
Line A
✘
Interface: Conventional systems transfer 64B on each access
Notes: 64B transfers
No partial-line transfers
due to internal bandwidth constraints

## Slide 8: Enabling TMC on commodity memories
Compressed Commodity Memory
Channel
Data A
Pair-wise remapping compression enables 2x effective bandwidth, and works on commodity DRAM
Line A
Line B
Line A
Line B
Retrieve two lines per access, and store into L3. If both lines useful, 2x effective bandwidth.
Access length unmodified.
✔
Approach: Relocate lines together in one location
Notes: Since we can’t change cacheline size, maybe we can get more lines per CL-sized access.
If both are useful, 2x effective bandwidth (with BW-free adjacent-line prefetch), while maintaining access length.
Enables 2x BW, and works on commodity DRAM.

## Slide 9: Overview
Background
Proposal
  Address Mapping
  In-line Metadata
  Location Prediction
Results
Dynamic Policy
Targeting Metadata Overhead

## Slide 10: Understanding metadata lookup
Line B
M=0
M
M
M
Read Request: Line B
Read Metadata, informs compressed mapping
Read location-1
Prior approaches rely on reading metadata first to learn mapping.
Costs bandwidth and latency
Line A
Line B
M=1
M
M
M
Line A
Location of B changes depending on compressibility
Uncompressed
Compressed
0
1
2
0
1
2
Read Metadata, informs uncompressed mapping
Read location-2
Double-access to read one line
Double-access to read two lines
Notes: Location of B changes depending on compressibility. Prior approaches need metadata to know where to look. Costs BW and latency.

## Slide 11: TMC with Metadata (+ METADATA Cache)
Chart: Speedup w.r.t Uncompressed
| fotonik | lbm17 | soplex | libq | mcf17 | milc | Gems | parest | sphinx | leslie | cactu17 | omnet17 | gcc06 | xz | wrf17 | bc twi | bc web | cc twi | cc web | pr twi | pr web | mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | SPEC | GAP | MIX
TMC (metadata) | 0.975 | 0.985 | 1.071 | 0.987 | 0.837 | 1.102 | 0.954 | 1.2 | 1.055 | 1.167 | 0.592 | 0.804 | 1.703 | 0.692 | 1.083 | 0 | 0.563 | 0.777 | 0.578 | 0.813 | 0.511 | 0.723 | 0 | 1.059 | 0.975 | 0.915 | 0.962 | 0.942 | 0.923 | 0 | 0.985 | 0.651 | 0.961
Ideal | 1.021 | 1.005 | 1.146 | 1 | 1.062 | 1.168 | 1.005 | 1.24 | 1.091 | 1.204 | 1.025 | 1.184 | 1.759 | 1.01 | 1.118 | 0 | 1 | 1.044 | 1.003 | 1.005 | 1 | 1.004 | 0 | 1.099 | 1.116 | 1.061 | 1.086 | 1.063 | 1.091 | 0 | 1.124 | 1.009 | 1.086
TMC suffers from constantly accessing metadata
Evaluated on 8-core with 2 channels of DRAM
Metadata Lookup limits performance
(41% slowdown)
SPEC
GAP (Graph)
MIX
Slowdown on average
Notes: Metadata lookup hinders performance. Even with dedicated metadata cache.

## Slide 12: Insight: Can we Store Metadata in Line?
Line A
Line B
M
M
M
M
Read Request: Line B
Read Metadata, informs compressed mapping
Storing metadata with line, enables single-access mem read
Compressed
Read Line
Read Line and metadata
Single-access, avoid metadata lookup
Notes: The double access (for metadata) is harmful. Can we eliminate it? We can try storing metadata in line. 1 access to get both line and metadata.
Specifics as follows.

## Slide 13: In-line Compression-status Marker
Lines compressible together if size is <64B
Often, compressed lines don’t use all space
Insight: We can repurpose space inside compressed line to store a small 4-Byte marker that denotes compressibility
On reading a line with marker, we know it is a compressed line
Marker informs compressibility, without metadata lookup
4-byte marker
Line A
Line B
Invalid marker
Chart: % of Compressible Lines
| fotonik | lbm17 | soplex | libq | mcf17 | milc | Gems | parest | sphinx | leslie | cactu17 | omnet17 | gcc06 | xz | wrf17 | bc twi | bc web | cc twi | cc web | pr twi | pr web | average
Double ≤ 64B | 4.648 | 1.264 | 26.534 | 0.002 | 47.015 | 24.697 | 6.12 | 58.164 | 22.844 | 28.239 | 13.1 | 62.695 | 99.939 | 13.88 | 36.969 | 0 | 95.458 | 89.233 | 22.776 | 61.943 | 17.663 | 57.92 | 0 | 37.672
Double ≤ 60B | 4.642 | 1.257 | 24.394 | 0.002 | 33.384 | 24.695 | 6.098 | 56.142 | 22.089 | 28.23 | 12.122 | 52.704 | 99.914 | 12.093 | 36.193 | 0 | 95.444 | 88.082 | 19.294 | 58.635 | 15.786 | 56.82 | 0 | 35.62
0xdeadbeef
Can spare 4B cheaply
Notes: How to make space for metadata:
Compressible only if both lines fit to <60B instead. Ensures that 4B can be used to store metdata. Does not cost much compressibbility.
Repurpose for 4-byte marker. And separate invalid marker to avoid having multiple valid copies of data.
On reading line with marker, we know it is compressed line.
Marker informs compressibility, without metadata lookup

## Slide 14: Marker Collision
Line A
Line B
0xdeadbeef
Line A
0xdeadbeef
But, an uncompressed line could coincidentally store the marker value(we call this marker collision). 1 in 4 billion chance
?
?
Solution: Track lines that coincidentally store marker value in a small SRAM structure (16-entry table of colliding addresses).
See paper for more detailed collision analysis.
Small Collision Table (64B) is sufficient. Average time for collision table overflow is 10 million years.
Address A
Marker Collision Table
Notes: Marker collision (coincidental uncompressed line storing marker).
1/2^32 chance of collision.
Track lines that collide in small table
Average overflow time is 10 million years, and can change marker and recompress on such rare occurrences.

## Slide 15: Metadata with line, How to locate?
But, marker is with line. Don’t know where to access
Line A
Line B
0xdeadbeef
Invalid Marker
Line B
Line A
1
2
1
2
Uncompressed
Compressed
Reading all possible locations will waste bandwidth
Solution: We can Predict compressibility and location, to enable reading & interpreting line in one access
Find Line B
?
?
Single access
Single access
Notes: But, marker is with line. Don’t know where to look.
Reading all locations will waste bandwidth.
Can try to predict compressiblity and thus location. If accurate, single-access to read from compressed memory.

## Slide 16: Overview
Background
Proposal
  Address Mapping
  In-line Metadata
  Location Prediction
Results
Dynamic Policy
Targeting Metadata Overhead

## Slide 17: Page-based Line Location Predictor
Hash
Page Addr
M = 0
M = 1
M = 0
M = 1
Store last-compressibility seen
Predict Base indexing
Predict Compressed indexing
1
0
Page-based predictor achieves 98% location-prediction accuracy, by exploiting spatial locality in compressibility
Generally, lines within a page have similar compressibility
Notes: Exploit property that lines within page are likely storing similar data and thus have similar compressibility.
Last-time prediction good enough. Augment to per-page last-time prediction when multiple pages are accessed simultaneously.

## Slide 18: Verifying predictions with marker
Line A
Line B
0xdeadbeef
Invalid Marker
1
2
Compressed
Access Line B
Line A
Line B
0xdeadbeef
Invalid Marker
1
2
Compressed
Correct pred
Single-access, avoid metadata lookup
Double-access, some bandwidth overhead
Location
Predictor
Access Line B
Incorrect pred
Location
Predictor
Correct prediction
Incorrect prediction
Line B found
Line B not
found
Fortunately, mispredictions are rare
With in-line metadata and location prediction,
Practical TMC avoids most of the metadata overhead
Notes: Case 1 predict correctly. 1 access, find marker, avoid metadata lookup.
Case 2 predict incorrectly. 1 access, find marker telling you incorrect location, look up second location. Fortunately, rare.

## Slide 19: Overview
Background
Proposal
  Address Mapping
  In-line Metadata
  Location Prediction
Results
Dynamic Policy

## Slide 20: Methodology
Core Chip
  3.2GHz 4-wide out-of-order core
  8 cores, 8MB shared last-level cache
Compression
  FPC + BDI. Supports 4-to-1 also (see paper)
Commodity DRAM
CPU
Notes: 8-cores.
Compression algorithms used in this study were Frequent Pattern Compression and Base-Delta Immediate Compression. Algorithm used is orthogonal to study as any can be substituted.
4-to-1 compression also used (more in paper).

## Slide 21: Methodology
Commodity DRAM
 | Commodity DRAM
Capacity | 16GB
Bus | DDR1.6GHz, 64-bit
Channels | 2 channels
Bandwidth | 25 GBps
Latency | 35ns
CPU
Other sensitivities in paper
Notes: 2 channels of DRAM with DRAMSim2

## Slide 22: TMC and Practical TMC Performance
Chart: Speedup w.r.t Uncompressed
| fotonik | lbm17 | soplex | libq | mcf17 | milc | Gems | parest | sphinx | leslie | cactu17 | omnet17 | gcc06 | xz | wrf17 | bc twi | bc web | cc twi | cc web | pr twi | pr web | mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | SPEC | GAP | MIX
TMC (metadata) | 0.975 | 0.985 | 1.071 | 0.987 | 0.837 | 1.102 | 0.954 | 1.2 | 1.055 | 1.167 | 0.592 | 0.804 | 1.703 | 0.692 | 1.083 | 0 | 0.563 | 0.777 | 0.578 | 0.813 | 0.511 | 0.723 | 0 | 1.059 | 0.975 | 0.915 | 0.962 | 0.942 | 0.923 | 0 | 0.985 | 0.651 | 0.961
PTMC | 1.011 | 1 | 1.076 | 1 | 0.983 | 1.118 | 0.998 | 1.192 | 1.085 | 1.194 | 1.01 | 0.981 | 1.728 | 1.004 | 1.07 | 0 | 0.755 | 0.864 | 0.977 | 0.766 | 0.987 | 0.638 | 0 | 1.074 | 1.07 | 1.017 | 1.048 | 1.023 | 1.032 | 0 | 1.085 | 0.821 | 1.044
PTMC eliminates most metadata lookup to enable speedup
Significant Location Mispredictions  wastes bandwidth and latency
Evaluated on 8-core with 2 channels of DRAM. See paper for more workloads.
Inline-Metadata + Location-Prediction, eliminates metadata lookup
Metadata Lookup limits performance
SPEC
GAP (Graph)
MIX
Notes: PTMC eliminates most metadata–lookup with Line-Location Prediction and Inline-Marker.
However, some cases are still degraded.

## Slide 23: Overview
Background
Proposal
  Address Mapping
  In-line Metadata
  Location Prediction
Results
Dynamic Policy
Enabling Robust Performance

## Slide 24: bandwidth benefits/costs of compression
1
Useful
Prefetch
2
Relocating lines when compressibility changes
3
Location Misprediction
Should disable compression when costs outweigh benefits
Benefits
Costs
Line A
Line B
2 useful lines with 1 access
Line A
Line B
1 useful line with 2 accesses
Notes: Might want to turn off compression when hurts.
Benefits. Useful prefetch.
Costs. Multiple accesses to read lines (location misprediction). BW costs to relocate lines.

## Slide 25: Dynamic PTMC Implementation
Utility Counter observes if cost of compression is greater than benefit. If cost is greater, Dynamic-PTMC disables compression.
Can extend to multi-core with per-thread counters
Sampled Set
(always compress)
Enforce
Policy
Enable
Disable
Compaction
0
4096
Set 0
Set 1
Set 99
Increment Utility Counter
Decrement Utility Counter
2
3
1
Benefits
Costs
Set 1
Set 99
Set 1
Set 99
Note: disabling compaction for metadata-based approaches does not reduce metadata lookup
Notes: Sample. 1% of sets (or memory) always attempt compression. Observe benefit vs. cost. 99% compress or not depending on utility counter.
Can extend to multi-core
Note: does not work for metadata-based approaches. Prior approaches have needed to clean memory before it can confidently read a line without metadata access. Our approach on the other hand simply stops compressing lines together, and line location prediction accuracy will be naturally high as memory becomes mostly uncompressed.

## Slide 26: Dynamic PTMC Performance
Chart: Speedup w.r.t Uncompressed
| fotonik | lbm17 | soplex | libq | mcf17 | milc | Gems | parest | sphinx | leslie | cactu17 | omnet17 | gcc06 | xz | wrf17 | bc twi | bc web | cc twi | cc web | pr twi | pr web | mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | SPEC | GAP | MIX
PTMC | 1.011 | 1 | 1.076 | 1 | 0.983 | 1.118 | 0.998 | 1.192 | 1.085 | 1.194 | 1.01 | 0.981 | 1.728 | 1.004 | 1.07 | 0 | 0.755 | 0.864 | 0.977 | 0.766 | 0.987 | 0.638 | 0 | 1.074 | 1.07 | 1.017 | 1.048 | 1.023 | 1.032 | 0 | 1.085 | 0.821 | 1.044
Dynamic-PTMC | 0.987 | 1 | 1.059 | 1 | 0.999 | 1.104 | 1 | 1.192 | 1.087 | 1.192 | 1.01 | 1.002 | 1.722 | 1.004 | 1.07 | 0 | 0.997 | 1 | 1 | 0.997 | 1 | 0.996 | 0 | 1.064 | 1.058 | 1.021 | 1.045 | 1.025 | 1.038 | 0 | 1.084 | 0.998 | 1.042
Dynamic-PTMC ensures robust performance
(no slowdown across all workloads tested)
Disables compression when harmful (e.g. low location-prediction accuracy)
SPEC
GAP (Graph)
MIX
Notes: Removes all slowdown. Robust performance.

## Slide 27: Hardware Cost of proposed dynamic-ptmc
Memory controller modifications
  Compression / Decompression Logic
  Additional SRAM storage in controller
Dynamic-PTMC enables robust speedup with
minimal cost (276B SRAM, single-point modification)
 | SRAM Storage
Markers | 72B
Collision Table | 64B
Location Predictor | 128B
Dynamic-PTMC counter | 12B
Total Storage | 276B
Notes: Cheap
Modifications to memory controller. Compression/Decompression. Small SRAM storage.

## Slide 28: Practical Transparent Compressed Mem
Bandwidth Benefits
OS Transparent
Commodity Memory
Negligible Metadata Lookup
Robust Performance
Line A
Line B
0xdeadbeef
Invalid Marker
Location
Predictor
In-line Marker
Modified Mapping
✔
✔
✔
✔
✔
🗴
🗴
🗴
Thank you!
Dynamic Solution
Notes: Overview.
BW benefits. OS transparent with HW approach. Commodity memory with modified mapping. Remove metadata lookup with in-line marker and location prediction. And robust performance with dynamic solution.
Thank you.

## Slide 29: Additional Slides
Additional Slides

## Slide 30: Security of Markers
Marker Collisions where data stored matches marker
  We use 32-bit markers, which are created per-line and with a cryptographic collision-resistant hash. 1 / (2^32) chance of line coincidentally storing the same marker value. On average, memory space has one marker collision.
  We provision storing 16 of these exceptions, and overflowing is unlikely (> 10 million years per overflow event, assuming all of memory is written each nanosecond. On overflow, can change marker and recompress memory)

## Slide 31: Dynamic solution on prior metadata methods
Prior approach: Major cost is metadata access, which occurs even for incompressible lines. Even if you disable actively compacting lines, you still need to read metadata (until you clean all possibly compressed lines from memory).
Whereas, Dynamic-PTMC can disable compression costs by simply choosing not to actively compress data. Lines will be in uncompressed index and location will be easily predicted.

## Slide 32: Location prediction accuracy vs. metadata cache hit-rate
72% metadata cache hit-rate, vs 98% location pred.
Prior approaches pay high BW overhead for metadata

## Slide 33: Enabling 4-to-1 compression
On write: Reorganize compressed lines together in mem
  Restrict to 3 possible remappings (4-to-1, 2-to-1, uncompressed)
On read: lines have 1-3 possible locations and compression status
A
B
C
D
A
C
B
D
C
D
A
B
A
B
C
D
A
B
C
D
2:1 compressed
uncompressed
4:1 compressed
Possible locations:
1
2
2
3
  Page-based Last-compressibility Line Location Predictor still effective. Need additional 4-to-1 marker value.
B has two possible locations

## Slide 34: Invert line on collision: only compressed lines store marker
x44444444
x0 . . . . . . . . . . . . . . . . 44444444
Marker
x1 . . . . . . . . . . . . . . . . BBBBBBBB
Inverted line
Invert on collision
Line inversion
Table
-
-
-
A
Update
LIT
Line to install in mem addr A
Marker Collision ?
Do: &
1
2
1
2
Install as is
Yes
No
Store uncompressed lines that store marker value, in inverted form. Only compressed lines have marker.
(Reduces collision table check for compressed lines)