## Slide 1
Moinuddin Qureshi
Aditya Rohan, Gururaj Saileshwar, Prashant Nair
HYDRA: Enabling Low-Overhead Mitigation of Rowhammer
at Ultra-Low Thresholds via Hybrid Tracking

## Slide 2: Rowhammer Attacks
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 3: Rowhammer Attacks
Bit-Flips in Neighboring Rows
Row
Row
Row
Row of Cells (8KB)
Victim Row
Aggressor Row
Aggressor Row
DRAM
Rowhammer Attack
Rapid
Accesses
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 4: Rowhammer Attacks
Bit-Flips in Neighboring Rows
Row
Row
Row
Row of Cells (8KB)
Victim Row
Aggressor Row
Aggressor Row
DRAM
Rowhammer Attack
Rapid
Accesses
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Software Adversary Can Flip Bits in Page Tables &
Gain Kernel Privileges (Take Over a System)
[Seaborn+, Blackhat’15]
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 5: Rowhammer is Getting Worse!
Rowhammer Threshold: Bitflips require activating at least one row TRH times
Solutions must tolerate not only current TRH but future TRH (Our goal: TRH
30x Reduction in TRH in 8 years!
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 6: Typical Mitigation for Rowhammer
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
Targeted Row Refresh (TRR) in DDR4 (2015)

## Slide 7
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
TRResspass Breaks TRR Tracker [Frigo+, SP’20]
Source: The Hacker News
Blacksmith Attack: All DDR4 DRAM Vulnerable [Jattke+, SP’22]
Source: The Register
Typical Mitigation for Rowhammer
Targeted Row Refresh (TRR) in DDR4 (2015)

## Slide 8
Victim Row
Aggressor Row
Victim Row
DRAM
Why Trackers Break?
Refresh Period: 64ms, Row-Cycle Time: 45ns
Activation Budget Per Bank: ~1.4 Million
The number attack rows increases inversely to Threshold, so does tracker state
RH Threshold | 1-Bank | 32-banks
100,000 | 14 | 448
10,000 | 140 | 4.5K
1,000 | 1400 | 45K
Max. Attack Rows

## Slide 9: Pitfall of SRAM-Based Trackers
SRAM-Based trackers incur impractical SRAM overheads at ultra-low thresholds
RH Threshold | Graphene (100% CAM) | TWiCE | CAT | D-CBF (Blacklist only) | Naive
32K | 5KB | 37KB | 25KB | 53KB | 3.8MB
500 | 340KB | 2.3MB | 1.5MB | 768KB | 2.3MB
250 | 679KB | >2MB | >2MB | 1.5MB | 2MB
SRAM-tables can be in memory controller (CAT) or inside DRAM chip (TRR)
Overheads for 16GB Rank (16 Banks, 8KB Rows)
Our goal is < 64KB SRAM per Rank

## Slide 10: Pitfall of DRAM-Based Trackers
DRAM-based trackers incur low SRAM storage but high performance overhead (25%)
Counter-Based Row Activation [Kim, Nair, Qureshi - CAL’14]:
Keep counters for ALL rows in a dedicated region in DRAM, cache counter-lines on-chip

## Slide 11: Goal
Develop secure and low-cost Rowhammer mitigation:
  Effective at Ultra-Low thresholds (500 or below)
  Low SRAM overhead (<64KB per rank)
  Low performance overhead (< 1%)
  No changes to DRAM arrays or memory interfaces

## Slide 12: Observation and Insight
Rowhammer: Race against time (64 ms)
  Access many rows few times ✓
  Access few rows many times ✓
  Access many rows many times ✗
Applications (within 64ms): - Access 100k+ rows
- On average, few 10s of ACT/row
- Few thousand rows have 250+ ACT
Insight: - Have ability to track all rows (DRAM)
- Use SRAM to filter out common-case

## Slide 13: HYDRA: Hybrid Tracker
HYDRA: SRAM for group-tracking, and DRAM for per-row tracking (cached)
Address
Space
DRAM
Row Count Table (RCT)
Group Count
Table (GCT)
Memory Controller (SRAM)
Row Count
Cache (RCC)
Row-ID
HYDRA uses DRAM to get scalable tracking, and SRAM to avoid performance overheads

## Slide 14: HYDRA: Operation
Assume: Hydra Threshold = 250, Group Threshold= 200
Address
Space
DRAM
Row Count Table (RCT)
< 200?
Group Count
Table (GCT)
Row Count
Cache (RCC)
Row-ID
The GCT filters most of the counter checks, less pressure on RCC, minimal RCT access
Yes, Ctr++
No
Hit, Ctr++
Miss
32KB SRAM
(90.7% Accesses)
24KB SRAM
(9% Accesses)
4MB DRAM
(0.3% Accesses)

## Slide 15: HYDRA: Reset and Set
Every 64ms, Reset SRAM state
Address
Space
DRAM
Row Count Table (RCT)
Group Count
Table (GCT)
Memory Controller (SRAM)
Row Count
Cache (RCC)
Row-ID
HYDRA uses intelligent indexing to reduce RCT set overhead (128 counters in two lines)
When GCT-entry reaches 200
Set relevant RCT-entries to 200
If a Row is accessed continuously, first mitigation may be at 50, then 250 each
Up 200?

## Slide 16: Security Analysis
HYDRA Threshold is set to TRH/2 due to periodic reset (TH=250, TRH=500)
Proof that HYDRA issues a mitigation at-least once per TRH
Protection for RCT rows (their counters kept in SRAM, 500 bytes)
Protection against Half-Double (mitigations increment count for victim)
HYDRA works with any mitigating action (BH/RRS): Refresh 2 rows on each side
For detailed security analysis, please see the paper
Security NOT dependent on pattern

## Slide 17: Results
HYDRA has negligible slowdown (0.7%) and low SRAM overheads (57KB for two ranks)
Config: 8-core OOO, 32GB DRAM (2 Ranks, 8KB Row-Buffer)

## Slide 18: Say Hello! to DDR5
HYDRA provides scalable Rowhammer mitigation even for DDR5
SRAM overheads for 32GB (2 Ranks) for DDR4 (current) and DDR5 (soon)
Scheme | DDR-4 (16 banks/rank) | DDR-5 (32 banks/rank)
Graphene | 640 KB (CAM) | 1.3 MB (CAM)
TWiCE | 4.6 MB | 9 MB
CAT | 3 MB | 6 MB
D-CBF | 1.5 MB | 1.5 MB
HYDRA | 56.5 KB | 56.5 KB
DRAM overhead of HYDRA is negligible (4MB out of 32GB, 0.01%)

## Slide 19: Conclusion
Rowhammer is a moving target: Threshold keeps reducing (30x in 8 years)
Existing SRAM trackers needs unacceptable storage (at TRH
Existing DRAM-based tracker incurs unacceptable slowdown (25%)
We develop HYDRA, a hybrid tracker, that combines the best of both
  Ability to track arbitrary number of rows (good for security)
  Filter per-row updates using SRAM for group tracking (avoids slowdown)
HYDRA incurs 0.7% slowdown and needs 28KB/rank (at TRH=500)

## Slide 20: Sensitivity to GCT Capacity
A larger GCT virtually eliminates all slowdown (except for mitigating actions)
We use a default GCT of 32K

## Slide 21: Sensitivity to RH Threshold
HYDRA has can provide scalable Rowhammer mitigation even at low threshold
Structures scaled 2x for TRH=250, and 4x for TRH=125

## Slide 22: GCT vs RCC: Which One?
GCT is the primary source of effectiveness (filtering 90% of the accesses)

## Slide 23: D-CBF